# Functional Test Record
## SD card SPI bus and signal integrity
Configure an SD card to operate at fastest speed possible.

Procedure:
1. Perform 1M R/W test,
  1. Measure and record bus speed: __________
  2. Capture and record transaction beginning end such that timing can be seen, record two captures here
  3. Load the bus with another device
  4. Capture and record transaction beginning end such that timing can be seen, record two captures here

Criteria:
1. Does the SD car work alone, and with multiple devices? YES/NO
2. Does the other device also work? YES/NO
3. Do signals have sufficient setup and hold times? YES/NO
4. Are signals monotonic? YES/NO
## Check SD card CD function
Configure for SD card detection

Procedure:
With no card inserted, measure voltage on detect pin_____
1. With card inserted, measure voltage on detect pin_____
2. Recored pin configuration necessary here:

Criteria:
Do voltages fall outside ESP32 IO levels? YES/NO
## IMU
Configure the gyro and accelerometer for use and measure bus conditions. Make a program that continuously reads all 9 axes.

Peform the following during read loop:

Procedure:
1. Measure and record bus speed: __________
2. Capture and record transaction beginning end such that timing can be seen, record two captures here
3. Load the bus with another device
4. Capture and record transaction beginning end such that timing can be seen, record two captures here

Criteria:
1. Does the SD car work alone, and with multiple devices? YES/NO
2. Does the other device also work? YES/NO
3. Do signals have sufficient setup and hold times? YES/NO
4. Are signals monotonic? YES/NO
## Test IMU power features
Check the power reset capibility and ripple.

Procedure:
1. Run the "Read all axes" sketch
2. Capture power, data, clk lines at a glance, with attention to power verticle resolution, looking for load induced ripple. Record ripple: ________
3. Power the IMU down for the minimum _______ ms
4. Power the IMU back up
5. Read some IMU and Mag registers looking for default configurations

Criteria:
1. Is the power ripple acceptable? YES/NO
2. Did the IMU go to default values? YES/NO
3. Did the Mag go to default values? YES/NO
## Test the GPS port
Check that the serial pass-through is working fine

Procedure:
1. Loop-back the serial port
2. Run a program to return usb serial commands through the port
3. Capture a bit-variable character up to 115200 baud, measuring on the loopback
4. Measure the symbol rate for 9600, 57600, and 115200
  1. 9600: _____
  2. 57600: _____
  3. 115200: _____

Criteria:
1. Do the symbols have good integrity up to 115200? YES/NO
2. Is the symbol rate correct? YES/NO
## Test GPS module functionality
Expose GPS modules to the sky and check features

Procedure:
1. Attach 3 pin module.
2. Power device and wait for lock, record: _____
3. Record sample output:
4. Attach 4 pin module to holes
5. Power device and wait for lock, record: _____
6. Record sample output:

Criteria:
1. Does the cheap module work well? YES/NO
2. Does the expensive module work well? YES/NO
3. Is one module better than the other? YES/NO
## Test board power rails
Check that nothing is behaving stragely

For these tests, all functions should be running at greatest load

Procedure:
1. Measure ripple on power supply lines of shield
2. Attach current probe to isolate 3.3V rail
3. Measure full load power draw: _____
4. Switch board on and off
5. Measure 3.3V rail rise time: _____

Criteria:
1. Is the current draw acceptable for battery use? YES/NO
2. Is the rise time fast enough? YES/NO